## Slide 1
DAISY FIELD
OXI ONE MK1
SYNTHEX Project
Optimal Drum Machine
UX / UI Design
Hybrid architecture — Daisy Field as sound & performance surface
OXI One MK1 as sequencing brain · complete 3-layer control map
16
3×
24+
16
addressable controls
3×
parameter layers
DaisySP · libDaisy · MIDI Clock Sync · 3-State LED Encoding

## Slide 2
AGENDA
4 SECTIONS
01
Core UX Concepts
Drum machine design pillars, control paradigm taxonomy, immediacy principles
02
OXI One as Sequencing Brain
Function offloading, freed Daisy Field resources, MIDI clock integration
03
Daisy Field Implementation
3-state LED encoding, control layers, OLED architecture, firmware patterns
04
Full Control Map
Master parameter table, information density analysis, design rationale

## Slide 3
01
SECTION 01
Core UX Concepts
of Drum Machines
What separates immediate, performable hardware from menu-buried disappointments — the design principles every drum machine UI is evaluated against.

## Slide 4
THE 5 PILLARS OF DRUM MACHINE UX
1
IMMEDIACY
Zero-menu access to the most-used parameters. Volume, pitch, decay reachable in one gesture without mode changes. Cognitive latency from intention to action must be negligible.
2
VISUAL STATE
Every active state visible at a glance. Step-on LEDs, mute state, playback position, clock phase — all encoded in hardware. No screen navigation to read machine state.
3
LAYER ECONOMY
Second functions via hold/shift, not nested menus. Each additional layer doubles parameter space at zero hardware cost. Maximum 2 layers before muscle-memory breaks down.
4
TRANSPORT LOCK
Play/stop/record reachable without mode changes. BPM, pattern advance, fill always available during performance. No state machine dead-ends that require stopping to navigate.
5
VOICE FOCUS
One control context at a time. Selecting a voice reassigns all knobs to that voice immediately. Eliminates confusion of shared encoders with unclear selection state.

## Slide 5
CONTROL PARADIGM TAXONOMY
Three paradigms — cognitive load & performance profile
Paradigm
Device
Step Entry
Param Access
Visual Feedback
Daisy Field fit
Step-button
Roland TR-8S
Dedicated 16-step row
Knob-per-voice column
Step LEDs always-on
Low — paradigm mismatch: no step row
Pad / Groovebox
Novation Circuit
Pad grid dual-use
8 macro knobs + shift
RGB pad color coding
Med — closest form factor match
Encoder matrix
Elektron M:Samples
Trig key row
6 encoders + FUNC
OLED + trig LEDs
Low — OLED UX pattern useful
Hybrid (this design)
Daisy + OXI One
Offloaded to OXI
8 knobs × 3 layers
3-state key LEDs
Native — built for this target

## Slide 6
02
SECTION 02
OXI One as the
Sequencing Brain
Which functions the OXI One absorbs — and precisely what that liberates on the Daisy Field control surface.

## Slide 7
OXI ONE — FUNCTION OFFLOADING MAP
OXI ONE HANDLES
DAISY FIELD — FREED FOR:
Step Sequencing
DRUM mode — 8 gate outs, 16 steps per track, pattern chain, per-step probability
Transport
Play / Stop / Record, start/stop triggers, tap tempo encoder
Pattern Management
20 projects × 16 patterns, arrangement/chain mode
Clock Distribution
MIDI clock 24ppq → Daisy MIDI IN, sync pulse output
MIDI Note Triggers
Note On per voice hit per step → Field receives for LED flash
CV / Gate Modulation
Mod lanes → OXI CV OUT → Daisy Field CV IN 1–4
All 16 keys become performance + status display (no step entry role)
SW1 / SW2 freed from transport → available for 2× layer expansion
Row A = voice mute/solo/select with persistent 3-state LED encoding
Row B = contextual: FX routing, pattern queue, step on/off editing
Trigger flash per Note On = real-time voice activity indicator
CV IN 1–4 = modulation targets driven by OXI modulation lanes

## Slide 8
03
SECTION 03
Daisy Field
Implementation
Complete UX architecture for the Daisy Field surface:
3-state LED system · control layers · OLED strategy · MIDI clock integration
HARDWARE INVENTORY
8× knobs K1–K8 + 9th hardware volume
16× keys with LED (Row A + Row B)
2× switches SW1, SW2
128×64 OLED display
CV IN 1–4 · CV OUT 1–2 · Gate IN/OUT
MIDI IN / MIDI OUT (TRS 3.5mm)

## Slide 9
3-STATE LED ENCODING SYSTEM · 128×64px OLED FIELD
03 / Daisy Field Implementation
OFF
Slot empty / not in kit
Voice not assigned in current kit. Not sent by OXI in DRUM mode. No CPU overhead.
Empty FX slot
Unused voice position
Pattern slot void
~ ~
BLINK
Active but muted
OXI pattern running, voice silenced on Daisy. Blink phase toggles at 16th-note rate via MIDI clock 24ppq.
Muted during performance
Queued pattern (next)
FX bypass active
ON
Active and playing
Voice unmuted, playing steps. Solid-on between trigger flashes. Selected track in Row A.
Active voice playing
Selected track (Row A)
Current active pattern
80ms
FLASH *
Trigger hit — 80ms
Momentary override on Note On from OXI. Brightens to full for 80ms, returns to persistent LED state.
Beat accent indicator
Performance hit confirm
OXI step trigger
* FLASH is software-generated: duration distinguishes it from sustained ON. Driven exclusively by OXI MIDI Note On messages. No additional GPIO required.

## Slide 10
CONTROL MAPPING — NORMAL PLAY LAYER
SW1 released · SW2 released
K1–K8 · VOICE PARAMETERS
K1
LEVEL
Voice amplitude 0–100%
K2
PITCH
Tune / fundamental frequency
K3
DECAY
Envelope decay time
K4
PAN
Stereo position L–R
K5
FILTER
Low-pass filter cutoff
K6
REVERB
Reverb send level
K7
DELAY
Delay send level
K8
PROB
Step probability 0–100%
KEY ROWS · TRACK + STEP CONTROL
ROW A — VOICE SELECT (tap to select, knobs follow)
BD
SD
CH
OH
CP
TM
RM
FX
LED: ON = active/unmuted · BLINK = muted · OFF = empty · Bright-yellow = selected track
ROW B — STEP ON/OFF (steps 1–8 · SW2 tap = page 2 → steps 9–16)
1
2
3
4
5
6
7
8
Active step = yellow · Inactive step = grey · Tap to toggle. OXI reads the resulting pattern via Gate OUT.
SW1 hold → shift layer (knobs + Row A reassign) · SW2 tap → page flip 1–8 ↔ 9–16 · SW2 hold → pattern select SW1 + SW2 simultaneously → save current pattern

## Slide 11
CONTROL MAPPING — SW1 SHIFT LAYER
Hold SW1
Holding SW1 instantly reassigns K1–K8 and Row A from voice-centric to global/transport. Row B retains step 9–16 page role.
K1–K8 · GLOBAL / TRANSPORT
K1
BPM
Master tempo — live override of OXI clock master
K2
SWING
Global shuffle amount 0–100%
K3
MASTER VOL
Master output gain pre-DAC
K4
PAT LEN
Active pattern step length 1–16
K5
FILL PROB
Auto-fill trigger probability
K6
CLK DIV
Internal clock divider for slow voices
K7
GATE LEN
Global gate length override
K8
ACCENT
Velocity accent level for accented steps
ROW A · MUTE / UNMUTE
BD
SD
CH
OH
CP
TM
RM
FX
Tap while holding SW1 → toggle mute.
BLINK = muted (OXI running, Daisy silenced).
ON = active and passing audio.
ROW B · STEPS 9–16
9
10
11
12
13
14
15
16
Step row shifts to 9–16 context.
Toggle on/off same mechanics as normal layer.
Design principle: shift accessed by physical hold, not mode toggle — eliminates mode-lock. Release SW1 = instant return. OLED lines 3–4 update in real time to show shift parameter names.

## Slide 12
SW2 — STEP PAGE TOGGLE & PATTERN SELECT MODE
Tap · Hold
SW2 TAP · STEP PAGE FLIP (1–8 ↔ 9–16)
Each voice holds 16 steps. Row B (8 keys) displays one page of 8. SW2 tap flips pages. OLED Line 2 shows active page indicator.
PAGE 1 (steps 1–8) → SW2 tap → PAGE 2 (steps 9–16)
1
2
3
4
5
6
7
8
Active page
9
10
11
12
13
14
15
16
After SW2 tap
OXI One sequences both pages independently. Daisy displays only the page being edited. The OXI step cursor position is shown on OLED Line 2 — freeing Row B purely for toggling, not for displaying playback position.
SW2 HOLD · PATTERN SELECT MODE
Row A + Row B become 16-slot pattern selector.
LED states encode pattern status across all 16 slots.
Row A — patterns 1–8
1
2
3
4
5
6
7
8
Row B — patterns 9–16
9
10
11
12
13
14
15
16
Empty slot
Active (ON)
Queued (BLINK)
Release SW2 to load queued pattern on next bar boundary — seamless live switch aligned to OXI transport. Pattern LEDs provide persistent status: no screen interaction needed during performance.

## Slide 13
OLED 4-LINE DISPLAY ARCHITECTURE · 128×64px
03 / Daisy Field Implementation
BPM:128.0 SW:18% [PLAY]
TRK:BD PG:1/2 PROB:75%
LVL PIT DEC PAN FIL REV
DLY PRB · [SHIFT: OFF]
▌▌▌▌▌ ▌▌▌▌▌▌▌
8-voice level meters
LINE 1 — GLOBAL TRANSPORT
BPM, swing %, playback state. Always visible regardless of mode. Updated every MIDI clock tick.
LINE 2 — ACTIVE VOICE + PAGE
Selected voice name, step page (1/2), probability value. Updates on voice select or SW2 tap.
LINE 3 — K1–K6 ASSIGNMENT REMINDER
Abbreviated param names for K1–K6. Switches to shift-mode names on SW1 hold.
LINE 4 — K7–K8 + MODE STATE
K7–K8 labels + current shift state indicator. Eliminates need to memorize shift layer.

## Slide 14
MIDI CLOCK INTEGRATION — TEMPO-LOCKED LED FEEDBACK
OXI ONE
MK1
Master clock
24ppq MIDI
DAISY FIELD
MIDI IN
Parse clock
& Note On
LED HANDLER
(firmware)
blink_phase[]
flash_timer[]
TRS MIDI
24ppq + NoteOn
BLINK SYNC
tick % 6 == 0 → toggle blink_phase
= 16th-note tempo-locked blink
TRIGGER FLASH
NoteOn → flash_timer[v] = 80ms
Returns to persistent state after
// Called in MidiHandler — runs at interrupt priority
void OnMidiMessage(MidiEvent msg) {
if (msg.type == TimingClock) {
if (++midi_tick % 6 == 0) // 16th note
blink_phase = !blink_phase;
}
if (msg.type == NoteOn) {
int v = NoteToVoice(msg.data[0]);
if (v >= 0)
flash_timer[v] = 80; // 80ms flash
}
}
// In main loop: key_state[v] = flash_timer[v]>0 ? LED_ON : (muted[v] ? LED_BLINK : LED_ON)

## Slide 15
FULL CONTROL MAP — INFORMATION DENSITY SUMMARY
Control
Normal layer (SW1 off)
SW1-shift layer (hold)
SW2 held (pattern)
K1
Level — voice amplitude
BPM — master tempo
—
K2
Pitch / tune
Swing amount
—
K3
Decay time
Master volume
—
K4
Pan L–R
Pattern length
—
K5
Filter cutoff
Fill probability
—
K6
Reverb send
Clock divider
—
K7
Delay send
Gate length
—
K8
Step probability
Accent level
—
Row A (×8)
Voice select BD–FX
Mute / unmute toggle
Pattern select 1–16
Row B (×8)
Steps 1–8 on/off edit
Steps 9–16 on/off
Steps 9–16 on/off
SW1
Hold = shift active
—
—
SW2
Tap = page 1↔2 flip
Steps 9–16 context
Hold = pat. select
SW1 + SW2
Save current pattern
—
—
13
physical controls
3
interaction layers
24+
unique functions
3
LED states / key

## Slide 16
Key Takeaways
01
OXI One absorbs all sequencing complexity — freeing every Daisy Field key for performance state display rather than step entry.
02
3-state LED encoding (OFF / BLINK / ON) plus trigger flash delivers 4 distinct voice states per key with zero additional hardware.
03
Shift-hold (SW1) doubles knob parameter space without mode-lock — layer is physical, not logical, so muscle memory is preserved.
04
MIDI clock sync from OXI makes blink tempo-musical — muted voice indicators pulse in time, turning a UI cue into a performance aid.
05
OLED as persistent cheat sheet — 4-line format eliminates the need to memorize shift functions, reducing cognitive overhead mid-performance.
SYNTHEX Project · DaisySP · libDaisy · OXI One MK1 · 2026